IEEE Consumer Electronics Society
The Cloud meets Bluetooth Smart
Joe Decuir
Standards Architect, CSR
Bluetooth Internet Working Group chair

---
Agenda
Agenda
Wireless Applications Perspective
How do wireless devices spend energy?
What is Bluetooth Low Energy?
- How do the components work?
- How low is the energy?
What is Bluetooth Low Energy good for?
How the Cloud can find and drive Smart sensors
Where can we learn more?

---
IEEE Consumer Electronics Society
Wireless Perspective

---
Short range wireless applications areas
Short range wireless applications areas
	Voice	Data	Audio	Video	State
Bluetooth ACL / HS	x	Y	Y	x	x
Bluetooth SCO/eSCO	Y	x	x	x	x
Bluetooth low energy	x	x	x	x	Y
Wi-Fi	(VoIP)	Y	Y	Y	x
Wi-Fi Direct	Y	Y	Y	x	x
ZigBee	x	x	x	x	Y
ANT	x	x	x	x	Y
State = low bandwidth, low latency data
Low Power

---
How do wireless devices spend power?
How do wireless devices spend power?
Duty Cycle: how often they are on
The wireless world has put a lot of effort into reducing this
Protocol efficiency: what do they do when on?
Different MACs are tuned for different types of applications
TX power: how much power they transmit
And how efficient the transmit amplifier is
How long they have to transmit when they are on
Data rate helps here – look at energy per bit
How much energy the signal processing consumes
- This is driven by chip silicon process if the DSP dominates
- This is driven TX power if the RF dominates
Bluetooth Smart is low energy because it is simple, and OFF most of the time.

---
IEEE Consumer Electronics Society
How does Bluetooth Low Energy work?
Also Known as Bluetooth Smart™

---
What is Bluetooth Low Energy?
What is Bluetooth Low Energy?
A new radio, new protocol stack and a new profile architecture.
It’s designed to run from coin cells
It’s designed to support an Apps Store model
The Bluetooth SIG calls this “Smart Ready”
Designed to be LOWEST cost and EASY to implement
Prediction: Bluetooth Low Energy will be to Smartphones what USB has been to desktop PCs: universal peripheral connectivity
Wi-Fi Direct will cover high rate connectivity

---
Enable the Internet of Things
Enable the Internet of Things
- Mostly new PHY; some parts derived from the classic Bluetooth radio
- New advertising mechanism, for ease of discovery & connection
- Asynchronous connection-less MAC: used for low latency, fast transactions
  - As little as 3ms from start to finish for a transaction
- New Generic Attribute Profile (GATT) to simplify devices and the software that uses them.
- Asynchronous Client / Server architecture

---
Bluetooth low energy factsheet
Bluetooth low energy factsheet
Range:	~ 150 meters open field
Output Power: ~ 10mW (10dBm)
Max Current:	~ 15mA
Latency:	3 ms
Topology:	Star
Connections: > 2 billion
Modulation:	GFSK @ 2.4 GHz
Robustness:	Adaptive Frequency Hopping, 24 bit CRC
Security:	128bit AES CCM
Sleep current:	~ 1µA
Modes:	Broadcast, Connection, Event Data Models Reads, Writes
Specification or Implementation specific

---
Bluetooth low energy factsheet #2
Bluetooth low energy factsheet #2
Did you notice something missing?
Data Throughput
For Bluetooth low energy, data throughput is not a meaningful parameter. It does not support streaming.
It has a data rate of 1 Mbps, but is not optimised for file transfer.
It is designed for sending small chunks of data (exposing state).

---
Designed for exposing state
Designed for exposing state
11:24 am
20.5°C
49.6 km/h
Gate 6a BOARDING
2.4 bar
PLAY >>
2.7 kWh
Network Available
It’s good at small, discrete data transfers.
Data can triggered by local events.
Data can be read at any time by a client.
Interface model is very simple (GATT)

---
What are the pieces?
What are the pieces?
Controller
Host
Apps
Generic Access Profile
Generic Attribute Profile
Attribute Protocol
Security Manager
Logical Link Control & Adaptation Protocol
Host Controller Interface
Physical Layer
Link Layer
Direct Test Mode
Applications = Profiles & Services

---
Component descriptions
Component descriptions
Generic Access Profile (GAP) – establishes rules for connection
  - Find the device; find the services; set up security
- Generic Attribute Profile (GATT) and Attribute Protocol (ATT)
  - Client/server model
  - Attributes: Services, Characteristics, Descriptors
- Security Manager (SM)
  - Encryption is strong: AES-128
  - Key generation is weak, but will met FIPS requirements soon
- Logical Link Control and Adaption Protocol (L2CAP)
  - the multiplexer
- Link Layer (LL) – rules for using the radio
  - See summary in slides 22-25
- Physical Layer (PHY – how to deliver bits
  - See summary on slide 21

---
How does it work: new radio
How does it work: new radio
2.4 GHz ISM band, same as IEEE 802.11
1 Mbps GFSK
Larger modulation index than classic Bluetooth
40 Channels on 2 MHz spacing:

---
How does it work: new Link Layer
How does it work: new Link Layer
Low Complexity
1 packet format
2 Protocol Data Unit types: Advertising, Data Channel
7 Advertising Protocol Data Unit Types
7 Link Layer Control Procedures
Useful Features
Adaptive Frequency Hopping
Low Power Acknowledgement
Very Fast Connections

---
How does it work: advertising
How does it work: advertising
150µS
150µS
< 10mS
< 10mS
Peripheral
ADV_IND
ADV_IND
ADV_IND
SCAN_RSP
Central
SCAN_REQ
Channel 37
Channel 38
Channel 39
T_advEvent
Advertising event
Devices can advertise for a variety of reasons:
To broadcast promiscuously
To transmit signed data to a previously bonded device
To advertise their presence to a device wanting to connect
To reconnect asynchronously due to a local event

---
How it works: peripheral states & central states
How it works: peripheral states & central states
Central / Observer
Scanning
Advertising
Standby
Standby
Initiating
Connecting
Peripheral /Broadcaster
Connecting
A Broadcaster cannot enter the Connecting state.
An Observer cannot enter the Initiating State.

---
How does it work: data transactions
How does it work: data transactions
> 1.25mS
150µS
Periph.
Slave
ADV_IND
Etc.
Central
Master
Master
CONNECT_REQ
Channel 37
Data Channel
Connection event
Advertising event
Once a connection is made:
Master informs slave of hopping sequence and when to wake
All subsequent transactions are performed in the 37 data channels
Transactions can be encrypted
Both devices can go into deep sleep between transactions.

---
Sample transaction timing
Sample transaction timing
Time, usec	Master TX	Active time, usec	Slave TX
0		176	Advertise
326	Connect Request	352
Time for advertising on other channels, if needed
1928	Empty Packet (ACK)	80
2158		144	Handle Value Notification
2458	Empty Packet (ACK)	80
2683		96	Termination request
2928	Empty Packet (ACK)	80

---
How low can the energy get?
How low can the energy get?
Try calculating energy per transaction
- Assume an upper bound of 3 ms per minimal transaction
- Est TX power is 15mW (mostly TX power amp for 40 nm chips).
- (New chips will drop TX power below 8mw)
- For 1.5v battery, this is 10ma. 0.015 W x .003 sec = 45 micro Joules
How long could a sensor last on a battery?
- An example battery: Lenmar WC357, 1.55v, 180mAh, $2.
- 180mAh/10ma = 18 hours = 64,800 seconds = 21.6M transactions
- Suppose this sensor sends a report every minute = 1440/day
- For just the BT LE transactions, this is 15,000 days, or >40 yr
- This far exceeds the life of the battery and/or the product
In fact, the communication cost will be only part.
- This sensor could run on scavenged power, e.g. ambient light.
- Leakage currents put upper limits on battery life.

---
Your mileage may vary
Your mileage may vary
The previous slide calculated 45 uJ for the minimum transaction
- This number is an upper bound because it budgets 15mW for the entire 3 ms time, although the radio time is much smaller
- OTOH, more complex transactions may need more radio traffic
The low duty cycle on both sides depends on having a clock that gives each device an approximate time to wake up and transact business
- This can be as simple as a 32kHz oscillator, like watches
- The client/scanner/listener needs to wake up earlier and listen longer to accommodate clock frequency skew
- This is a common feature in CSR and some competing chips
The sensor itself draws power. That energy might exceed the power spent on the wireless link.
Wild card: leakage! As we move toward smaller on-chip geometries, leakage goes up quickly.

---
Scavenged power: electromechanical
Scavenged power: electromechanical
I saw a demo in India:
  - On/Off switch that runs on scavenged power
  - The switch rotates a magnet in a coil
  - There is enough energy to power a BT LE sensor that emits advertizing: turn ON, turn OFF
  - A control that listens for those message turns on lights, or any other device
- No batteries required
- This saves a lot of copper in the walls, too.

---
Scavenged Power: photovoltaic
Scavenged Power: photovoltaic
- I shopped for small photovoltaic converters.
- Example: 24x22 mm, producing 3.4v at 12ma.
  - Scale that by half, to 24x11 mm, to produce 1.7v at 12ma.
- That can power a Bluetooth Smart sensor indefinitely, if illuminated.
- Add a small (<50mAH) rechargeable battery (or capacitor) so it works under various conditions, and in the dark.
- Example use: break in detector on windows
- Example use: indoor location, with GPS coordinates

---
How does it work: Attribute Protocol (ATT)
How does it work: Attribute Protocol (ATT)
Clients and Servers
- Servers expose Attributes
- Clients use them
16 bit address space of handles – address within a device
Each attribute has a Universal Unique ID (UUID) – what it is?
- 16-bit if standardized by the Bluetooth SIG
- 128-bit if invented by the manufacturer
- Note: that manufacturers can add value without waiting for the SIG
The protocol supports a handful of actions:
- Clients: Discover or Find, Read, Write, Confirm an Indication
- Servers: respond to Client actions, Notification and Indication

---
How does it work: Generic Attribute Profile
How does it work: Generic Attribute Profile
Simple Servers
Those servers provide attributes:
- Characteristics, and descriptors for those characteristics
- Services: which can include characteristics and/or other services
Expose the state of the server.
Allows choice of security level: 128 bit AES CCM optional
Use the Attribute Protocol for transport
Defines Data Formats:
- Low Energy encapsulates all of the protocols and formats into the core. This makes profile development much faster and easier.
- The format is easy to encode in XML.

---
IEEE Consumer Electronics Society
What is Bluetooth Low Energy good for?

---
What is Bluetooth Low Energy Good for?
What is Bluetooth Low Energy Good for?
Connecting the things we carry with us:
- Watches: remote display from other devices
- Tags: locate or track objects (e.g. warning if you walk away)
- Health & fitness sensors (e.g. pedometer in your shoes)
- Body sensors (e.g. blood pressure, pulse rate, blood glucose, etc)
Accessing the things around us:
- Fobs: use proximity as a security/access control means
- Home and office automation
Low duty cycle M2M communication:
Sensors and controls in homes, offices and factories
Communication within a system
Car to car wheels/tires
Connecting anything that has intrinsic data to the Internet

---
What are the Use Cases?
What are the Use Cases?
- Automation I/O
- Environmental Sensing
- Battery status
- Heart rate monitor
- Physical activity monitor
- Blood glucose monitor
- Cycling sensors
- Pulse Oximeter
- Health Thermometer
- Proximity
- Time
- Emergency
- Network availability
- Personal User Interface
- Simple remote control
- Browse over Bluetooth
- Temperature Sensor
- Humidity Sensor
- HVAC
Most of these were standardized in the last 3 years

---
Amplified: Smart Ready systems
Amplified: Smart Ready systems
The majority of the ‘smartphones’ sold have the ability to download applications that can drive Bluetooth Smart peripherals.
  - iOS6, iOS7, later Android systems, WinPH8
- Current market sizes:
  - 370 million in 2012
  - Nearly a billion in 2013
  - Most new tablets, and newer PCs, are Smart Ready, too.
- The Bluetooth Smart ‘Appcessory’ market has the wind behind it!

---
Appcessory usage model
Appcessory usage model

---
IEEE Consumer Electronics Society
Introduce the Cloud

---
It’s about the Internet of Things
It’s about the Internet of Things
Things have data
&
Web Services want this data
Bluetooth Smart provides the technology to connect these two.

---
Bluetooth Smart needs Gateways
Bluetooth Smart needs Gateways
Devices that support Bluetooth Smart Gateway functionality need to provide a transparent pipe from a device to or from an IP address.
  - Middleware at the IP address can access the device directly as if it were a collector talking to it locally.
  - The Gateway device plays no part other than in acting as a pipe.
- Standards are being developed now for three gateways types:
  - The Cloud meets Bluetooth Smart Sensors – just published
  - The Smart Sensors can reach the Cloud
  - The Smart Sensors have IPv6 built in.

---
The Cloud meets Smart Sensors
The Cloud meets Smart Sensors
This technique is the most general:
  - The cloud reaches the device through a gateway
  - The Internet client + the gateway impersonates a standard Bluetooth client
  - It works with existing sensor designs
- Use the GAP RESTful API to find and configure the sensor device
- Use the GATT RESTful API to operate the sensor device
- The Bluetooth SIG just published these whitepapers this month.

---
Smart Sensors reach the Cloud
Smart Sensors reach the Cloud
This technique required the device to understand the cloud
  - The Bluetooth Smart client + the gateway impersonates a standard web client
- The Bluetooth Smart client will use the Bluetooth HTTP Proxy Service.
  - This is in development and testing
  - Prediction: Adopted and published this year

---
Another kind of Gateway: 6LoWPAN
Another kind of Gateway: 6LoWPAN
There is an RFC (Request for Comment) in the IETF (Internet Engineering Task Force) to implement 6LoWPAN over Bluetooth Low Energy/Bluetooth Smart™.
  - 6LoWPAN is a variant of IPv6 with features like header compression
- The Bluetooth Low Energy (Core version 4.1) radio will be used, with a feature that allows Connection Oriented Channels in the L2CAP multiplexer, bypassing ATT/GATT.
- A 6LoWPAN (IPv6 stack) would be implemented in a leaf node.
  - TLS (IP security for IPv6) should also terminate in this stack.
- The applications would be native Internet Applications, such as those defined in many aspiring higher level standard.
  - Prediction: tested and Adopted this year

---
How does a RESTful Gateway work?
How does a RESTful Gateway work?
Four essential components:
1. Embedded web site, which exposes web pages for each attached device
2. GAP API translator engine
3. Embedded IPv6 security module, which translates Bluetooth Security Manager key generation and encryption to IPv6 security
4. GATT API translator engine

---
GATT API architectural layers
GATT API architectural layers
- A gateway device has a connection to the Internet.
- Each gateway device may have one or more Bluetooth Smart Nodes connected. Each Node will have a 48-bit MAC address.
- Each Node will have one or more embedded Services. Each Service has an identifying UUID. An entire Service is delimited by a pair of 16-bit handles.
- Each Service shall include one or more Characteristics, and may contain Secondary Services.
- Each Characteristic is identified by a UUID, and contains a value. Each Characteristic may include one or more (Characteristic) Descriptors.
- Each Descriptor has a UUID and a value.

---
GATT RESTful API general form
GATT RESTful API general form
Command: {GET|PUT|EventSource}
http://<gateway>/node/<node>/service/<service>/characteristic/
<characteristic>/value
- A {command} is given to an http program
- <gateway> is the root URI - Universal Resource Identifier
- node is a program that manages Smart devices
- <node> is the name of a particular Smart device
- serv is a program that manages services
- <services> is the name of a particular Service
- char is a program that manages characteristics for a given service
- <characteristic> is the name of a particular characteristic
- desc is a program that manages descriptors
- val is a program that manages characteristic and descriptor values

---
Example RESTful GATT API syntax
Example RESTful GATT API syntax
Find a primary service given the URI for a <gateway>, and a connected Smart device node:
GET http://<gateway>/node/<node>/serv/priority=1
Read a Characteristic value:
GET http://<gateway>/node/<node>/serv/<service>/char/<characteristic>/val
Write a Characteristic value:
PUT http://<gateway>/node/<node>/serv/<service>/char/<characteristic>/val
Enable Characteristic Notifications:
PUT http://<gateway>/node/<node>/serv/<service>/char?notify=1
Get last Characteristic Indication:
GET http://<gateway>/node/<node>/serv/<service>/char/val?indicate=1

---
Apply RESTful GATT API to manage a home
Apply RESTful GATT API to manage a home
- Start with the Bluetooth Automation Service in testing now.
- The service defines 5 kinds of I/O ports:
  - Digital Inputs and Digital Outputs
  - Analog Inputs and Analog Outputs
  - Aggregate Inputs
- It also provides for setting trigger values.

---
Define a home automation example
Define a home automation example
Some sample definitions:
- a <gateway> “98027” (author’s zip code)
- a home management node called “hmgr”
- an Automation IO Service called “home”
- a single digital input called “alarm”
- a single digital output called “lock”
- a single analog input called “temp-sense”
- a single analog output called “temp-set”

---
Apply the RESTful API to this example
Apply the RESTful API to this example
Find the Services at Home:
GET http://98027/node/hmgr/serv?priority=1
Read the Alarm status:
GET http://98027/node/housemgr/serv/home/char/alarm/val
Lock the doors:
PUT http://98027/node/hmgr/serv/home/char/lock/val/1
Read the current temperature:
GET http://98027/node/hmgr/serv/home/char/temp-sense/val
Set the desired temperature:
PUT http://98027/node/housemgr/serv/home/char/temp-set/val/<value>

---
Gateway application exposes a Server
Gateway application exposes a Server
This could be an existing device upgraded.

---
Mobile client reaches a Server
Mobile client reaches a Server

---
Makers can used Bluetooth Smart
Makers can used Bluetooth Smart
BLEduino
Bluno = BLE with Arduino
Web search: BLE Arduino Shield

---
IEEE Consumer Electronics Society
Summary
Predictions
Resources

---
Summary
Summary
Bluetooth Smart works.
The power is low enough to support coin cells and scavenged power.
Bluetooth Smart is past the hype curve peak.
- It will enable a lot of accessories
- It will enable a lot of applications that use them
Bluetooth Smart will be to mobile devices what USB is to Personal Computers
The new RESTful APIs will allow web clients to reach Bluetooth Smart server devices.
- This will allow networks of Bluetooth Smart devices
- It will allow the development of heterogeneous networks

---
Calls to Action
Calls to Action
Learn about Bluetooth Low Energy
  - Ask questions
  - See the references
  - Read the books
- Think about how to use it to satisfy market needs
  - The list of use cases is just a start
- Find partners to add value
  - There were dozens of companies tested the draft specifications for interoperability
  - There are many hardware and firmware vendors
- Joint the Bluetooth SIG – www.bluetooth.org
  - It cost nothing but IP rights to join as an Adopter – you can read technical announcements, read FRD and you get prototype specifications
  - It cost money to join as an Associate, but then you can participate in the technical work – we are subject to non-disclosure rules!

---
Questions?
Questions?

---
Resources:
Resources:
SIG site: http://www.bluetooth.com/Pages/bluetooth-smart-devices.aspx
The Bluetooth 4.1 specification:
https://www.bluetooth.org/DocMan/handlers/DownloadDoc.ashx?doc_id=282159
Current work – if you are a Bluetooth SIG member:
http://www.bluetooth.com/enhancements
White Papers:
Bluetooth GAT REST API, www.Bluetooth.org
Bluetooth GATT REST API, www.Bluetooth.org
Internet Connectivity Solutions for BT Smart, www.sensinode.com
IPv6 Security, www.infosec.gov.hk/English/technical/files/ipv6s.pdf
Articles:
Introducing Bluetooth Smart, IEEE CES Magazine: Part 1: a look at classic and new technologies, January 2014; Part 2: Applications and Updates, April 2014
Books:
- Essentials of Short Range Wireless, by Nick Hunn
- Bluetooth Low Energy – a Developer’s Guide, by Robin Heydon.

---
My contact information
My contact information
Joe Decuir
Issaquah, WA USA 98027
IEEE: jdecuir@ieee.org
Distinguished Lecturer, IEEE Consumer Electronics Society
Vice chair, IEEE Global Humanitarian Technology Conference, www.ieeeghtc.org
Membership development, Seattle Section
Work: joe.decuir@csr.com
Standards Architect, CSR Technology
Chair, Bluetooth Internet Working Group